## Slide 1
ASSIST HEIDI · Co-Creation Project
Marua: Taking Pictures
and Videos
Wheelchair-mounted stabilizer with Bluetooth remote
for hands-free photography and video recording
Seagirls 🌊 · Natálie · Alina · Markéta
Est. cost: ~€90 · MIT / CC BY 4.0

## Slide 2
The Problem that needed solution
Who is Marua and what did she need?
Seagirls 🌊 | ASSIST HEIDI
Marua, 30 — Wheelchair User
Diagnosis: Myoclonic Epilepsy
Primary impairment: Uncontrollable tremors and twitching of the hands Remaining abilities: Can press large buttons even with limited fine motor control Cognition: Fully capable, communicates without difficulty
Her Request
Goal: Take stable photos & videos — including while moving The solution needed to:
Mount phone to wheelchair frame
Stabilize phone independently of hand movements
Trigger shutter without touching phone
Switch between photo and video mode
Work while wheelchair is in motion

## Slide 3
The Solution
Two-part assistive technology device
Seagirls 🌊 | ASSIST HEIDI
Part 1 — Smartphone Stabilizer
Loc-Line arm (3/4")
Flexible modular hose — holds phone at any angle
Magnetic phone adapter
Quick attach/detach — works with any smartphone
Wheelchair clamp
Screw-tightening — fits any standard wheelchair frame
Part 2 — Bluetooth Remote
Adafruit Feather V4
BLE + LiPo charging built-in, USB-C
LiPo battery (3.7V 800mAh)
Rechargeable, JST connector
3D-printed enclosure
Openable — easy component swap, PLA ~3.5h print

## Slide 4
The Solution
Two-part assistive technology device
Seagirls 🌊 | ASSIST HEIDI
Part 1 — Smartphone Stabilizer
Part 2 — Bluetooth Remote

## Slide 5
How It Works
Setup & controls at a glance
Seagirls 🌊 | ASSIST HEIDI
Setup — 5 Steps
1
Clamp Loc-Line arm to wheelchair frame
2
Attach magnetic adapter to arm end
3
Stick magnetic sticker on phone, attach phone
4
Turn on remote, pair via Bluetooth
5
Open camera app → use remote
🎮 Controls
Button 1
— Shutter
take photo
start/stop video
Button 2
— Mode
front camera↔rear camera
Bluetooth HID · C++ · VS Code

## Slide 6
Technical Overview & Cost
Reproducible by anyone with a 3D printer
Seagirls 🌊 | ASSIST HEIDI
Chart: Cost Breakdown (Total ~€90)
| Loc-Line arm | Feather V4 | Mag. adapter | LiPo battery | Enclosure + buttons
Cost (€) | 50 | 20 | 10 | 7 | 3
Key Specs
3D Print
PLA · Prusa MK4S · ~3.5h
CAD
Onshape (open link in docs)
Firmware
C++ · Bluetooth HID · VS Code
MCU
Adafruit Feather V4 (BLE + LiPo)
Weight
Lightweight — no added strain
License
MIT (code) · CC BY 4.0 (docs)
Tools needed: 3D printer · Soldering iron · USB-C cable · PrusaSlicer · VS Code

## Slide 7
Lessons Learned
What worked, what we'd do differently
Seagirls 🌊 | ASSIST HEIDI
What went well
Loc-Line arm is extremely flexible and stable — perfect for this use case.
Bluetooth HID approach worked without any custom app on the phone.
Magnetic phone adapter made mounting effortless.
Improvement suggestions
Key takeaway
Involve the user at every step — Marua's feedback shaped the final button size and placement critically.
Simple solutions beat complex ones in AT design.
Switching between photo mode and camera
Improvement of stability
Would add a charging indicator LED next version

## Slide 8
Thank You!
Questions?
Seagirls 🌊 · Natálie · Alina · Markéta